## Slide 1: IPv6 The Internet’s Future?
  Barry O’Donovan
  Engineers Ireland - April 25th 2012
  https://www.inex.ie/ei-ipv6-2012.html

## Slide 2: INEX
  An IXP – Ireland’s IP Peering Hub
  Neutral, industry owned association
  Founded 1996; ~66 members; 5 PoPs

## Slide 3: INEX
  An IXP – Ireland’s IP Peering Hub
  Neutral, industry owned association
  Founded 1996; ~66 members; 5 PoPs
  https://www.inex.ie/joining/aboutixps
  https://www.inex.ie/about/memberlist

## Slide 4: Barry O’Donovan
“Internet Infrastructure Specialist”
MD of Open Solutions
“Closet geek; political anorak, husband, father, network enginner, company owner, employer, …”
  http://www.barryodonovan.com/
  http://www.opensolutions.ie/

## Slide 5: Overview
A (brief?) history of Internet numbering
IPv4 exhaustion status
Introduction to IPv6
Why IPv6 adoption is sooooooooooo slow
The IPv6 opportunity

## Slide 6: Overview
A (brief?) history of Internet numbering
IPv4 exhaustion status
Introduction to IPv6
Why IPv6 adoption is sooooooooooo slow
The IPv6 opportunity

## Slide 7: The Problem
Why IPv6?
Because we’ve run out of addresses
Again!
Huh? Really!?
Yes, we’ve been here before!

## Slide 8: Internet Time Machine
1969: ARPANET commissioned by DoD
1970: ARPANET hosts start using NCP:
Network Control Protocol [RFC33]
8 bit addressing
=> only 256 hosts!

## Slide 10: Internet Time Machine
1972: Telnet specification [RFC318]
1973: Ethernet outlined in a PhD Thesis
File Transfer specification [RFC454]
1976: Queen Elizabeth sends an email!

## Slide 11: Internet Time Machine
1982: DCA & ARPA establish TCP and IP
DoD declares TCP/IP as their standard
1983: Cutover from NCP to TCP/IP (IPv4)
“Flag Day” – January 1st 1983
  RFC2235 – Hobbes’Internet Timeline

## Slide 12: “Flag Day” January 1st 1983
All nodes updated on Flag Day to IPv4
(still “facepalm”?)
8bit addresses -> 32 bit addresses
~4.29 billion addresses
Enough?
No: 7.008 billion people; 8.01 by 2025
1 billion “smart devices” shipped in 2011

## Slide 13: Back Up the Truck
Are we all clear on what an IP address is?
“A number assigned to a device on a network”
We’ve all seen them:
127.0.0.1 192.168.1.254 8.8.4.4
DNS: www.engineersireland.ie => 46.22.128.85

## Slide 14: Who’s the Boss?
RIRs – Regional Internet Registries
IANA
AfriNIC
APNIC
RIPE
LACNIC
ARIN
LIRs – Local Internet Registries
eircom
Vodafone
Blacknight
End Users

## Slide 15: Overview
A (brief?) history of Internet numbering
IPv4 exhaustion status
Introduction to IPv6
Why IPv6 adoption is sooooooooooo slow
The IPv6 opportunity

## Slide 16: What’s Left?
IANA
AfriNIC
APNIC
RIPE
LACNIC
ARIN
Feb 3rd 2011
Apr 15 ‘11

## Slide 17: What’s Left?
IANA
AfriNIC
APNIC
RIPE
LACNIC
ARIN
Feb 3rd 2011
Apr 15 ‘11
Late 2012
Late 2013
Mid 2014
Mid 2015
Final /8 policies:
once only - /22 (1024) – must have IPv6
~16k allocations (>7k LIRs in RIPE 2010)

## Slide 18: What’s Left?
IPv4 exhaustion projection is a presentation in its own right
If you want to know more:
Geoff Huston - http://www.potaroo.net/
  http://www.potaroo.net/tools/ipv4/index.html

## Slide 19: What’s Left?
IPv4 exhaustion projection is a presentation in its own right
If you want to know more:
Geoff Huston - http://www.potaroo.net/
  http://www.potaroo.net/tools/ipv4/index.html

## Slide 20: Overview
A (brief?) history of Internet numbering
IPv4 exhaustion status
Introduction to IPv6
Why IPv6 adoption is sooooooooooo slow
The IPv6 opportunity

## Slide 21: IPv6
IETF began developing IPng in…
1993!
RFC1883 Internet Protocol, V6, Specification
(1995)
IETF Standard 1998 (RFC2460)

## Slide 22: IPv6 in the OSI Model?
Physical
Data Link
IPv4
TCP UDP ICMP
Application
Physical
Data Link
IPv6
TCP UDP ICMP
Application

## Slide 23: What’s New in IPv6
It’s (only?) an evolution of IPv4
Extended address space
32bit addresses => 128bit addresses
~4.29 billion => ~340 undecillion
Huh?
340,282,366,920,938,000,000,000,000,000,000,000,000

## Slide 24: What’s New in IPv6
Stateless autoconfiguration (and RD)
Simplified header
Removed on-the-fly fragmentation
No more ARP – Now ICMPv6 ND
Native Security, Flow labels & IPsec

## Slide 25: IPv6 Addressing
128 bits / 16 bytes: 8 x 16bit hex blocks
2001:0db8:0000:0000:0702:b33f:001b:0055
2001:0db8::0702:b33f:001b:0055
2001:db8::702:b33f:1b:55
2a01:268:3002::35

## Slide 26: IPv6 Subnetting
340 undecillion addresses is a bit misleading…
Typical initial LIR allocation is /32.
2001:0db8

## Slide 27: IPv6 Subnetting
340 undecillion addresses is a bit misleading…
2001:0db8:0000:0000:0702:b33f:001b:0055
64 bit interface ID
18,446,744,073,709,551,616 addresses – 18.4 “quintillion”.
ISP end user assignment /48 (/56)
65,536 /64 subnets at end user.
Typical initial LIR allocation is /32. 65,536 /48 end users / sites

## Slide 28: IPv6 in the “Real World”
It’s been around and live for a long time!
“If the end user ever needs to know about IPv6 then we’ve made a complete f&%k up of the transition.”
All current operating systems support it. Natively and by default.
Even Windows!

## Slide 29: IPv6 in the “Real World”
It’s been around and live for a long time!
“If the end user ever needs to know about IPv6 then we’ve made a complete f&%k up of the transition.”
All current operating systems support it. Natively and by default.
Even Windows!

## Slide 30: IPv6 in the “Real World”
Most services have long supported IPv6
SMTP, POP3, IMAP, DNS, HTTP(s), SSH, Telnet, FTP, Bit Torrent, IRC, IM, …
Modern systems default to IPv6
(e.g. DNS AAAA lookups before A)

## Slide 31: IPv6 in the “Real World”
barryo@destiny:~ $ host www.opensolutions.ie
www.opensolutions.ie has address 87.232.16.35
www.opensolutions.ie has IPv6 address 2a01:268:3002::35
barryo@destiny:~ $ host -t MX opensolutions.ie
opensolutions.ie mail is handled by 10 mail.opensolutions.ie.
barryo@destiny:~ $ host mail.opensolutions.ie
mail.opensolutions.ie has address 87.232.16.61
mail.opensolutions.ie has IPv6 address 2a01:268:3002::61
So what’s the problem…?

## Slide 32: Overview
A (brief?) history of Internet numbering
IPv4 exhaustion status
Introduction to IPv6
Why IPv6 adoption is sooooooooooo slow
The IPv6 opportunity

## Slide 33: Transition to IPv6
IPv6 is not backwards compatible with IPv4
A second “Flag Day” is impossible
That leaves two real choices:
(a) Dual stack networking (medium term)
(b) CGNs, CDNs, ALGs (medium -> long term)

## Slide 34: Dual Stack Transition
Running IPv4 and IPv6 in parallel
Already in place for modern OS’
Already in place for modern (ISP) routers
Firewalls & L7 Devices Caught/Catching Up
Main issues are: access network and CPEs
And demand.
And we still have IPv4.

## Slide 35: Back Up the Truck. Again.
We should probably talk about
ISP networking

## Slide 36: Back Up the Truck. Again.
We should probably talk about
ISP networking

## Slide 37: Back Up the Truck. Again.
We should probably talk about
ISP networking
And
“The Internet”

## Slide 38: Back Up the Truck. Again.
We should probably talk about
ISP networking
And
“The Internet”
Our ISP
Content
Transit Providers

## Slide 39: Back Up the Truck. Again.
We should probably talk about
ISP networking
And
“The Internet”
Our ISP
Content

## Slide 40: Back Up the Truck. Again.
We should probably talk about
ISP networking
And
“The Internet”
Our ISP
Content

## Slide 41: Back Up the Truck. Again.
We should probably talk about
ISP networking
And
“The Internet”
Our ISP
Content

## Slide 42: Dual Stack Transition
We said:
“Main issues are: access network and CPEs”
From what we just learned,
where are we with IPv6 transition?

## Slide 43: Back Up the Truck. Again.
We should probably talk about
ISP networking

## Slide 44: Dual Stack Transition
We said:
“Main issues are: access network and CPEs”
From what we just learned,
where are we with IPv6 transition?
Our ISP
Content
Transit Providers

## Slide 45: Transition to IPv6
Next issue: Demand.
End user demand – have you asked your ISP?
Your IT vendors? RFTs?
Access Provider  Content Provider
Need IPv6 content that users demand
Need IPv6 users that content providers need

## Slide 46: Transition to IPv6
Next issue: Demand.
End user demand – have you asked your ISP?
Access Provider  Content Provider
Need IPv6 content that users demand access to
Need IPv6 users that content providers need to reach

## Slide 47: Transition to IPv6
How do we solve “chicken and egg” problem?
It’s actually quite easy…
But painful… and slow…
We wait.
IPv4 is running out. Fast.
We need to aggressively push / demand IPv6
We need to avoid CGNs / CDNs / ALGs

## Slide 48: Irish ISPs and IPv6 Ripeness
  http://ripeness.ripe.net/
RIPE have an IPv6 RIPEness project
Up to 4 stars assigned for:
Having an IPv6 allocation
Visibility in routing tables
Having a “route6” object
Having a reverse DNS delegation

## Slide 49: Irish ISPs and IPv6 Ripeness

## Slide 50: Irish ISPs and IPv6 Ripeness

## Slide 51: Irish ISPs – Top Performers

## Slide 52: World IPv6 Day – June 8 ‘11
Top websites & ISPs turned on IPv6
Google, Facebook, Yahoo!, Akamai, Limelight
“To see what would happen…”
Microsoft (and xbox, bing); 100+ million users
“Almost no connectivity issues”
“Brokenness was within the margin of error”

## Slide 53: World IPv6 Launch – June 6 ‘12
Permanently enabling IPv6
Google, Facebook, Yahoo!, Akamai, Limelight
Microsoft, AT&T, D-Link, Cisco

## Slide 54: World IPv6 Launch – June 6 ‘12
Permanently enabling IPv6
Google, Facebook, Yahoo!, Akamai, Limelight
Microsoft, AT&T, D-Link, Cisco

## Slide 55: Overview
A (brief?) history of Internet numbering
IPv4 exhaustion status
Introduction to IPv6
Why IPv6 adoption is sooooooooooo slow
The IPv6 opportunity

## Slide 56: The IPv6 Opportunity
IPv6
“The Powerhouse of the Internet’s Future”
Hmmm…
Well certainly enabling the Internet’s future
We’re all aware of the benefits of the Internet
But what advantages does IPv6 offer?

## Slide 57: The IPv6 Opportunity
More address space.
Auto-configuration (local and routable).
Return to end-to-end networks. Woot!
i.e. no more NAT!
“An Internet of Devices”
IPv6 is built to scale – no manual intervention

## Slide 58: The IPv6 Opportunity
Network merges – renumbering (and VPNs)
More efficient routing
More efficient packet processing
Directed Data Flows & Multicast

## Slide 59: The IPv6 Opportunity
To sum it up:
IPv6 is about the future;
And future possibilities.

## Slide 60: Overview
A (brief?) history of Internet numbering
IPv4 exhaustion status
Introduction to IPv6
Why IPv6 adoption is sooooooooooo slow
The IPv6 opportunity
Getting starting with IPv6

## Slide 61: Getting Started with IPv6
Ask your ISP for IPv6
They’ll probably say no. Do it anyway!
Then goto a “tunnel broker”
SixXS: http://www.sixxs.net/
Hurricane Electric: http://www.tunnelbroker.net/
6to4 - 6rd - Teredo

## Slide 62: That’s All Folks!
  Copy of the Presentation:
  https://www.inex.ie/ei-ipv6-2012.html
Contact me:
Barry O’Donovan
barry@opensolutions.ie
INEX: https://www.inex.ie/